## Slide 1: PYTOTUBE: DUAL PHSYICS SOLVER FROM SCRATCH
With (Scientific) Python Language

## Slide 2: Why Python?
Extremely powerful
  Numerical Computation (numpy)
  Visualizing
  Parallel processing (including CUDA, and OpenCL)
  Image processing
  GUI development
  Interactive Computing lik (and better than) MATLAB with IPython.
Notes: Python is developer friendly and easy and also powerful language for scientific computation.
Portable: runs all OS
Modern: Object oriented, Interactive computing like MATLAB, GUI Development, coding standards makes highly readable code writing.

## Slide 3: Why Python?
It is developer (scientist) friendly BECAUSE:
  You feel very comfortable as developing it MATLAB.
  Interpreted, NOT compiled. You don’t need to compile and link. Just code and run. Developing an extremely computationally intensive programs is better in Assembly but DO NOT worry because Python is a powerful glue language to integrate extensions written in other languages.
Portable (Runs both Windows and Linux without pain.
Modern
  Object oriented
  Well-suited to modern-day application (unit testing, GUI development, readable coding, OOP, etc.)

## Slide 4: APPLICATION DESIGN
And planning according to future plans

## Slide 5: Programming Requirements
Reusable : Modular
  So any application can use a part of code
Easy Extensible for Multi Physics : Object oriented
  Solver algorithms/Mesh types/Any Physics must be added dynamically, seamless and painless.
Well documented
Version Control System : Git
  Source Version Control System is a MUST of software development process.
Notes: Since we are being developing a dual (and multi) physics software it MUST be
Highly Modular and easy extensible,
Object Oriented design makes software a little bit slow, but it is needed for complicated software, and it makes easy thinking of app design

## Slide 6: Version Control GUI for Git

## Slide 7: Short Term Scientific Requirements
2D Transient Laplace Solver for Velocity and Temperature Fields
Dual physics (Heat and Flow) and Free/Forced Convection in 2D
Simple Optimizations
Polar / Cylindrical Coordinates Support
Simple Radiation modelling
Essential heat and flow boundary-initial conditions modelling
Simple couplings
Sparse matrices for performance

## Slide 8: Long Term Requirements
Geometry/Mesh import from common formats (Paraview, Fluent, Gridgen)
Automatic meshing with Netgen Lib
Switching from Finite Differences to Finite Elements.
Extensive Radiation modelling
Advanced boundary-initial condition input. (polynomial, function, etc)
Turbulent modelling
Topology optimization

## Slide 9: Finite Element Scheme
Node based approach, finite differences method with node based scheme.
In Laplace2d class, energy approach is used with cell based scheme. Cell based means that one temperature represents a cell.
T(i)
T(i+1)
1D node based approach
2D cell based approach
T(i, j+1)
T(i,j)

## Slide 10: Application Design
Classes must separated with the respect of scientific branches.
Fluid mechanics / Math / Heat Transfer
Don’t repeat yourself law.
For the maintainability and reusability.
class Heat1d(Laplace):
Heat1d is inherited from Laplace class, means Heat1d class owns all properties of Laplace class. Laplace class designed/planned as it would be used as any Partial Differential Equation in the form of Laplacian Equation.

## Slide 11: Matrice Solving Method
At now, we are not considering performance issues. So We solve the matrices by
solve(A,B) or inv(A)*B

## Slide 12: Which Boundary Conditions Implemented in Laplace Eqn.?
Steady State Laplace Equation

## Slide 13: Dirichlet BC
def dirichlet(self, index, Scalar):
Call with
  EXAMPLE.dirichlet(index=0, Scalar=Value) # or EXAMPLE.dirichlet(0, Scalar=Value) # or EXAMPLE.dirichlet(0, Value)

## Slide 14: Neumann BC
def neumann(self, index, Value):
Call with
  EXAMPLE.neumann(index=0, Value=99.0) # or
  EXAMPLE.neumann(0, Value=99.0) # or
  EXAMPLE.neumann(0, 99.0)

## Slide 15: Which Boundary Conditions Implemented in 1D Heat Equation
Steady State 1D Heat Equation

## Slide 16: Symmetry-Adiabatic / Constant Heat Flow
If K=0 symmetry or adiabatic line.
K>0 Fixed heat flow enters the Control Volume
K<0 Fixed heat flow leaves the Control Volume

## Slide 17: Symmetry / Constant Heat Flow
def Conduction(self, x, k):
Call with
EXAMPLE.Conduction(x=0.0, k=-10.)
I don’t know why I named this method as ‘Conduction’ 
Future correct forms would be
def Symetry(self, x, k=0): #and
def FixedHeatFlow(self, x, k):
Heat1d.Conduction method calls Laplace1d.Neumann method

## Slide 18: Convection
def Convection(self, x, k, h, Ta):
Call with:
EXAMPLE.Convection(x=1.0, k=75., h=125.0,Ta=200.0)

## Slide 19: Fixed Temperature
def Temperature(self, x, T):
Call with:
EXAMPLE.Temperature(x=0.0, T=700.)
Heat1d.Temperature method calls Laplace1d.Dirichlet method
I am planning add a feature that Temperature (Dirichlet) BC in 2D, can be given a user defined/linear/polynomial/exponential functions of x and y. This should give more flexibility to model/approximate real situations in Thermal Analysis. In addition, node by node BC giving also is a good feature to model complex systems as simple problems.

## Slide 20: Source
An now, source method supposes that, heat generation is uniform and all elements generates heat. A feature must be added in 2D such that a source can be given a few nodes. It is more realistic than now.
EXAMPLE.source(k=WATER_K, Q=7.5e4)

## Slide 21: A simple Example
from pytotube import Heat1d
Q = Heat1d(L=1.0, N=5)
WATER_K = 70.
Q.source(k=WATER_K, Q=7.5e4)
Q.Conduction(x=0.0, k=0.)
Q.Convection(x=1.0, k=WATER_K, h=500., Ta=300.)
Q.solve()
Q.plot()
Q.ax.set(title=r'Temperature Distribution')

## Slide 22: A simple Example

## Slide 23: A simple Example
>>> Q.A
array([[ 1., -1., 0., 0., 0., 0.],
[ 1., -2., 1., 0., 0., 0.],
[ 0., 1., -2., 1., 0., 0.],
[ 0., 0., 1., -2., 1., 0.],
[ 0., 0., 0., 1., -2., 1.],
[ 0., 0., 0., 0., 70., -170.]])
>>> Q.B
array([[ 0. ],
[ -42.85714286],
[ -42.85714286],
[ -42.85714286],
[ -42.85714286],
[-30000. ]])

## Slide 24: Analogy with Heat Transfer and Irrotational Flow
2d Potential Flow
2d Heat Transfer
Convection Heat Transfer

## Slide 25: Analogy with Heat Transfer and Irrotational Flow
2d Potential Flow
Along a constant we have
2d Heat Transfer
This is similar to isothermal contour lines, and conservation of energy.

## Slide 26: Analogy with Heat Transfer and Irrotational Flow
2d Potential Flow
These equations seems like
2d Heat Transfer
Thermal Resistance

## Slide 27: Roadmap to Dual Physics
Solving simultaneously heat transfer and fluid flow

## Slide 28: Method
Conservation of mass
Conservation of Energy
Conservation of Linear Momentum

## Slide 29: Conservation of mass

## Slide 30: Conservation of Energy (Energy Equation)

## Slide 31: Conservation of Linear Momentum

## Slide 32: Comments and Recommendations
Laplace1d and Heat1d was only simple trial of solving Laplace equation with Finite Differences.
And experimenting the difficulties developing a general use solver and algorithms with Python/Numpy.
And picking a numerical scheme, numerical method, building a small application structure and drawing a roadmap for PDE solving.
And comparing different approaches with engineering and numerical problems
  Energy Approach / Finite Differences
  Node based / Cell Based
2D solver is serious work because, 2D PDE result are more meaningful than 1D, and often more than 3D analysis.

## Slide 33: Comments and Recommendations
To sum up, all of these works in 1D are only a meeting with:
Numpy/Optimization Tools
Numerical methods/schemes
PDE solving Finite Elements/Volumes/Differences
Problem solving and developing algorithm
Developing a tested and documented scientific application with a software engineer approach.

## Slide 34: 2D Laplace Equation
(1,1)
(1,2)
(1,3)
(1,4)
…
(1,NX)
…
(NY,NX-1)
(2,NX)
(NY,NX)
…
…
…
…
(NY,1)
(NY,2)
(NY,3)
(NY,4)
X
Y

## Slide 35: Indexing
0
1
2
3
…
NX-1
…
…
2 × NX-1
NY × NX-1
NX
…
I × NX + J
…
(NY-1)×NX
…
…
…
X
Y